## Slide 1
OmniDMA: Scalable RDMA Transport over WAN
Kai Lv, Jinyang Li, Pengyi Zhang, Heng Pan, Luyang Li, Shuihai Hu, Zhenyu Li, Gaogang Xie, Jingbin Zhou, and Kun Tan

## Slide 2
Growing Demand for Cross-Geolocation Transport
Distributed tasks require high-performance geo-distributed transport
For efficient data replication and freshness
Cross DCI / DC-WAN / WAN
Geo-distributed Cloud Services
LLM training
Database
Storage
Data
moving
Federated
learning
Decentralized
RL
Distributed service
Datacenters
Cloud edge
Private Servers
etc.
Software transport faces bottlenecks
struggles to keep up with growing Ethernet bandwidth
RDMA offers promising performance
High bandwidth, low CPU overhead

## Slide 3
Hard to Deploy RDMA in Wide Area Networks
Hard to maintain a lossless WAN
RDMA is vulnerable to packet loss
while
Packet loss is inevitable in WAN
Congestion loss
Random loss
Large RTT (& BDP) worsens go-back-N
Large feedback delay
Excessive spurious retransmissions
PFC is unsuitable in WAN
Large headroom required
Need network-wide replacement
Incompatible with CUBIC-like CC
Dedicated devices is costly & hard to scale
Need infrastructure updates
Low radix
* NVIDIA Metrox-3 XC Long-Haul InfiniBand. https://nvdam.widen.net/s/ggdj8tqdgf/infiniband-datasheet-metrox-3-xc-long-haul-2380143
NVIDIA MetroX-3 XC long haul system*
RoCEv2 goodput over different distance & loss rate
Reliability can be expensive and exclusive…
Can RDMA support end-to-end loss-tolerant transport?

## Slide 4
Revisit Selective Retransmission (SR)
Limitations of existing bitmap designs under large RTT & BDP
Per-QP bitmap: limited by RNIC SRAM capacity; falls back to GBN when exhausted.
Shared bitmap pool: hard to support QP Context swapping, limiting QP scalability.
Host-side bitmap: handle out-of-order (which dominate in WAN) in host; got CPU bottleneck.
SR: RDMA tracks packet arrival with bitmap window
Window size constrains in flight packet count and throughput.
How to scale the reorder window without sacrificing scalability?

## Slide 5
Observation #1: Concentrated Packet Drops
throughput
time
Network
capacity
Congestion losses
Congestion control’s AIMD policy
Long feedback delay
Loss / ACK / RTT / ECN / …
Tail drop in WAN is bursty and consecutive
Large delay -> untimely rate adjustment -> buffer exhaustion -> bursty (non-uniform) packet drop
For AIMD CCs: periodically packet drop
Record consecutive losses as a block to optimize space utilization
Large BDP requires scalable loss recording

## Slide 6
Observation #2: Coupled Transmission and Retransmissions
Reorder window must support random packet arrival efficiently
Coupling Tx and Re-Tx in a unified window requires the bitmap in SRAM
Every single tier of Tx or Re-Tx is sequential
NACKs and retransmitted packets are generated sequentially
Predictable packet arriving pattern
Decouple Tx and each Re-Tx
leverage the predictable arrival pattern for offloading.

## Slide 7
OmniDMA Overview
Design 1: Adamap for loss recording
Record consecutive loss segments
Support both precise and range recording
Fix-size design for easier scheduling
Design overview
Design 2: 3-tier control path
Decouple transmission and retransmission(s)
Transport-driven context scheduling
Constant (and small) RNIC memory footprint

## Slide 8
Adamap
Capturing variable loss patterns with fixed-size data structure
Exploits spatial locality of losses
Combine precise and compact range representation
Adamap-driven selective retransmission
Piggybacked in NACK
Retrieve WQEs and generate packets according to Adamap contents

## Slide 9
3-tier Control Path
Tier 1: First-Time Transmission Handling
Detect losses
generate Adamap
Processing frequency: ~O(BW)
Tier 2: First-Retransmission Handling
Exploits the sequential pattern
Prefetch for line-rate processing
Processing frequency: ~O(BW × LossRate)
tail
head

## Slide 10
3-tier Control Path
Wait… Should we maintain a separate control path for every retransmission tier?
Unpredictable tier of retransmissions
Packets retransmitted > 1 times are rare
It is more cost-effective to manage all high-order retransmissions in a unified manner!

## Slide 11
3-tier Control Path
Tier 3: High-order Transmission Handling
Manage Adamap of high-order transmission with a unified lookup table
Lookup index pre-embedded in NACK and returns with retransmitted packets
O(1) Adamap access via direct table lookup
Characteristics of three-tier control path (BW: bandwidth; LR: loss rate)
To further overlap the access cost on critical path:
Intra-QP: dedicated queue
Inter-QP: QP interleaving and pipelining

## Slide 12
Evaluation
Topology
P2p connected by a switch
100Gbps, 1KB MTU
Setup
NS3 simulation
Long-haul link settings
Varied distance: 200m ~ 3000km
Loss rate: 0%, 0.1%, 0.2%, 0.5%, 1%, 2%, 3%
Loss distribution: Amazon Cloud Network[1]
Long-haul link
1us
Simulation topology
[1] Measuring and improving the reliability of wide-area cloud paths. (WWW’17)

## Slide 13
Preliminary Results
Distance-independent goodput
  Only affected by loss rate
Small loss-recording overhead
  RNIC mem: small & fixed
  Total mem: less than bitmap-only scheme
Limited critical-path DMA reads
  Can be further mitigated with caching & RNIC’s QP scheduling and pipelining
Evaluate performance, overhead and efficiency

## Slide 14
Summary
To enable scalable RDMA transport over WAN:
Motivation:
Utilize non-uniform packet loss pattern over WAN.
Decouple transmission and retransmission for an “unbounded” window.
Design:
Use Adamap to record loss segments, improving space efficiency.
Enable window scalability through Adamap linked-list offloading.
Manage high-order retransmissions uniformly with O(1) access overhead.

## Slide 15
Thank you

## Slide 16
Q & A